## Slide 1: Introduction to Cyber Security
COMP3134 Week 3

## Slide 2: Overview
Objective
  Passive and Active Sniffing
  Address Resolution protocol (ARP)
  ARP poisoning
  Media Access Control (MAC) address flooding
Main Teaching Points
  Listening/ monitoring / observation is intermediate step
  Exploitation is advanced step
Learning Outcome(s)
  Identify & baseline network traffic using network monitoring tools
  Identify and filter various protocols and network ports

## Slide 3: Network Sniffing

## Slide 4: Network Sniffing
Definition
  Process of monitoring and capturing data (packets) of a network
    Promiscuous mode
      Allows device to intercept and read each network packet that arrives in its entirety
  Sniffing is the process of monitoring and capturing all the packets passing through a given network using sniffing tools.
Comparison:
  Chat Room VS Instant Messenger
Significance / Risks
  Can see all traffic even if it was no intended for your network

## Slide 5: Network Sniffing Game
Groups of 3
2 people speak to each other sitting down
  Can move around in chair but stay seated
1 person listens 2 meters away write down all NOUNS you hear
  BONIS: write down name of person whom uttered the noun
Talk for 1 minute
30 seconds listener recaps nouns
Repeat until everyone was the listener once

## Slide 6: Key definitions
Hub
  All data is sent and received on all open ports (traffic broadcasted to all hosts)
Switch
  Knows which hosts to send specific message to and does so directly
Hub vs Switch
  Hub works on the physical layer (Layer 1) of OSI model
  Switch works on the data link layer (Layer 2).
  Switch is more efficient than the hub.
  Switch can join multiple computers within one LAN,
  Hub just connects multiple Ethernet devices together as a single segment.

## Slide 7: How Network Sniffing Works
Sniffer tools turns the Network Interface Card (NIC) of system to the promiscuous mode
A sniffer can continuously monitor all the traffic to a computer through the NIC by decoding the information encapsulated in the data packets.

## Slide 8: How Network Sniffing Works

## Slide 9: Network Sniffing: Passive Sniffing
Traffic is recorded but not altered
  Only listening
Hub devices
  traffic is sent to all the ports.
Network that uses hubs
  All hosts on the network can see the traffic.
    Therefore attacker can easily capture traffic
Hubs are almost obsolete
  Modern networks use switches.
Passive sniffing is no longer effective.

## Slide 10: Network Sniffing: Active Sniffing
Traffic is monitored and may be altered
Used to sniff a switch-based network.
Injects address resolution packets (ARP) into a target network to flood on the switch content addressable memory (CAM) table.
  CAM keeps track of which host is connected to which port.

## Slide 11: Network Sniffing: Active Sniffing
Active Sniffing Techniques (4)
  MAC Flooding
  DNS Poisoning
  Spoofing Attacks
  ARP Poisoning
(4) Protocols which are affected
  HTTP
  SMTP
  FTP
  IMAP

## Slide 12: Network Sniffing
Implication
  Open unused ports provide gateway to potential attackers
Application
  Various sniffing tools are used to accomplish network sniffing
    Wireshark
Demo
  Let’s look at Wireshark

## Slide 13: Address Resolution Protocol

## Slide 14: Address Resolution Protocol
Definition
  ARP is acronym
  Runs on data link layer (Layer 2) of the OSI model.
  Purpose is to resolve an IP address to a MAC address
    Every hardware connected to the Internet has a unique MAC address association

## Slide 15: Address Resolution Protocol

## Slide 16: Address Resolution Protocol
Host A wants to communicate with Host B with an IP 192.168.1.3.
Host A needs MAC address of Host B.
Host A will look inside its ARP table cache to search of Host B’s IP address
  If not present, Host A will send an ARP broadcast packet to every device on the network asking, “Who has Host B’s IP address?”
  Once Host B receives the ARP request, it will send an ARP reply telling Host A “I am Host B and here is my MAC address.”
  The MAC address would be then saved inside the ARP table.
Command to view ARP table
  arp -a

## Slide 17: Spoofing Game
Groups of 3
1 person is acting, 1 person is judge, 1 person is guessing
Actor
  Write down famous individual name and pass it to judge
  Speak like famous person BUT without uttering noun
Judge
  Determine if guesser correctly guessed OR actor violated noun-rule
1-minute rounds

## Slide 18: ARP Poisoning

## Slide 19: ARP Poisoning
Definition
  Also know as ARP Spoofing
  Get in the middle of regular communication.
Method
  Spoofed ARP reply sent to any host on a network
    Make it believe that a certain IP is associated with a certain MAC address,
      Thereby poisoning its ARP cache that keeps track of IP to MAC addresses.
Significance / Risks
  ARP protocol always trust reply is coming from correct device.

## Slide 20: ARP Poisoning

## Slide 21: MAC Address Flooding
Media Access Control

## Slide 22: MAC Address Flooding
Definition
  Send huge amount of ARP replies to a switch
    Thereby overloading the cam table of the switch.
  Once the switch overloads, it goes into hub mode
    It will forward the traffic to every computer on the network
Significance / Risks
  Switches behaving like hubs makes network sniffing easier

## Slide 23: Sniffing and Spoofing Counter Measurements
Static ARP
  Add IP-MAC address pairs manually
    Time-consuming
Port security
  Map each switch to port for sending and receiving
    Cisco = Dynamic ARP Inspection (DAI)
  Discards invalid IP-MAC address pairs
    Protections against DNS poisoning & spoofing

## Slide 24: Terms to Know
Passive and Active Sniffing
Address Resolution protocol (ARP)
ARP poisoning
Media Access Control (MAC) address flooding
Hub
Switch
Network Interface Card (NIC)
Promiscuous mode
Content addressable memory (CAM)

## Slide 25: Resources
Websites
  ARP Poisoning
    https://doubleoctopus.com/security-wiki/threats-and-tools/address-resolution-protocol-poisoning/
  MAC Address Flooding
    https://www.interserver.net/tips/kb/mac-flooding-prevent/
Videos
  Network Sniffing
    https://www.youtube.com/watch?v=gXTuTfOoFjg
  ARP
    https://www.youtube.com/watch?v=cn8Zxh9bPio